## Slide 1
TCP/IP Protocol Suite
<number>
قسم الحاسوب
المرحلة الرابعة - شبكات الحاسوب
مدرس المادة: م.نشوان السلام علي
Data Communications and Networking المصادر:
By Behrouz A.Forouzan

## Slide 2
TCP/IP Protocol Suite
<number>
4.2 CLASSFUL ADDRESSING
IP addresses, when started a few decades ago, used the concept of classes. This architecture is called classful addressing. In the mid-1990s, a new architecture, called classless addressing, was introduced and will eventually supersede the original architecture. However, part of the Internet is still using classful addressing, but the migration is very fast.
The topics discussed in this section include:
Recognizing Classes
Netid and Hostid
Classes and Blocks
Network Addresses
Sufficient Information
Mask
CIDR Notation
Address Depletion

## Slide 3
TCP/IP Protocol Suite
<number>
Figure 4.2 Occupation of the address space

## Slide 4
TCP/IP Protocol Suite
<number>
Table 4.1 Addresses per class

## Slide 5
TCP/IP Protocol Suite
<number>
Figure 4.3 Finding the class in binary notation

## Slide 6
TCP/IP Protocol Suite
<number>
Figure 4.4 Finding the address class

## Slide 7
TCP/IP Protocol Suite
<number>
How can we prove that we have 2,147,483,648 addresses in class A?
Example 5
Solution In class A, only 1 bit defines the class. The remaining 31 bits are available for the address. With 31 bits, we can have 231 or 2,147,483,648 addresses.

## Slide 8
TCP/IP Protocol Suite
<number>
Find the class of each address:
a. 00000001 00001011 00001011 11101111 b. 11000001 10000011 00011011 11111111 c. 10100111 11011011 10001011 01101111 d. 11110011 10011011 11111011 00001111
Example 6
Solution See the procedure in Figure 4.4. a. The first bit is 0. This is a class A address. b. The first 2 bits are 1; the third bit is 0. This is a class C address. c. The first bit is 1; the second bit is 0. This is a class B address. d. The first 4 bits are 1s. This is a class E address..

## Slide 9
TCP/IP Protocol Suite
<number>
Figure 4.5 Finding the class in decimal notation

## Slide 10
TCP/IP Protocol Suite
<number>
Find the class of each address:
a. 227.12.14.87 b.193.14.56.22 c.14.23.120.8 d. 252.5.15.111 e.134.11.78.56
Example 7
Solution a. The first byte is 227 (between 224 and 239); the class is D. b. The first byte is 193 (between 192 and 223); the class is C. c. The first byte is 14 (between 0 and 127); the class is A. d. The first byte is 252 (between 240 and 255); the class is E. e. The first byte is 134 (between 128 and 191); the class is B.

## Slide 11
TCP/IP Protocol Suite
<number>
In Example 5 we showed that class A has 231 (2,147,483,648) addresses. How can we prove this same fact using dotted-decimal notation?
Example 8
Solution The addresses in class A range from 0.0.0.0 to 127.255.255.255. We need to show that the difference between these two numbers is 2,147,483,648. This is a good exercise because it shows us how to define the range of addresses between two addresses. We notice that we are dealing with base 256 numbers here. Each byte in the notation has a weight. The weights are as follows (see Appendix B):
See Next Slide

## Slide 12
TCP/IP Protocol Suite
<number>
2563, 2562, 2561, 2560
Example 8 (continued)
Last address: 127 × 2563 + 255 × 2562 + 255 × 2561 + 255 × 2560 = 2,147,483,647
First address: = 0
Now to find the integer value of each number, we multiply each byte by its weight:
If we subtract the first from the last and add 1 to the result (remember we always add 1 to get the range), we get 2,147,483,648 or 231.

## Slide 13
TCP/IP Protocol Suite
<number>
Figure 4.6 Netid and hostid

## Slide 14
TCP/IP Protocol Suite
<number>
Millions of class A addresses are wasted.
Note:

## Slide 15
TCP/IP Protocol Suite
<number>
Figure 4.7 Blocks in class A

## Slide 16
TCP/IP Protocol Suite
<number>
Figure 4.8 Blocks in class B

## Slide 17
TCP/IP Protocol Suite
<number>
Many class B addresses are wasted.
Note:

## Slide 18
TCP/IP Protocol Suite
<number>
Figure 4.9 Blocks in class C

## Slide 19
TCP/IP Protocol Suite
<number>
The number of addresses in class C is smaller than the needs of most organizations.
Note:

## Slide 20
TCP/IP Protocol Suite
<number>
Class D addresses are used for multicasting; there is only one block in this class.
Note:

## Slide 21
TCP/IP Protocol Suite
<number>
Class E addresses are reserved for future purposes; most of the block is wasted.
Note:

## Slide 22
TCP/IP Protocol Suite
<number>
In classful addressing, the network address (the first address in the block) is the one that is assigned to the organization. The range of addresses can automatically be inferred from the network address.
Note:

## Slide 23
TCP/IP Protocol Suite
<number>
Given the network address 17.0.0.0, find the class, the block, and the range of the addresses.
Example 9
Solution The class is A because the first byte is between 0 and 127. The block has a netid of 17. The addresses range from 17.0.0.0 to 17.255.255.255.

## Slide 24
TCP/IP Protocol Suite
<number>
Given the network address 132.21.0.0, find the class, the block, and the range of the addresses.
Example 10
Solution The class is B because the first byte is between 128 and 191. The block has a netid of 132.21. The addresses range from 132.21.0.0 to 132.21.255.255.

## Slide 25
TCP/IP Protocol Suite
<number>
Given the network address 220.34.76.0, find the class, the block, and the range of the addresses.
Example 11
Solution The class is C because the first byte is between 192 and 223. The block has a netid of 220.34.76. The addresses range from 220.34.76.0 to 220.34.76.255.

## Slide 26
TCP/IP Protocol Suite
<number>
Figure 4.10 Masking concept

## Slide 27
TCP/IP Protocol Suite
<number>
Figure 4.11 AND operation

## Slide 28
TCP/IP Protocol Suite
<number>
Table 4.2 Default masks

## Slide 29
TCP/IP Protocol Suite
<number>
The network address is the beginning address of each block. It can be found by applying the default mask to any of the addresses in the block (including itself). It retains the netid of the block and sets the hostid to zero.
Note:

## Slide 30
TCP/IP Protocol Suite
<number>
Given the address 23.56.7.91, find the beginning address (network address).
Example 12
Solution The default mask is 255.0.0.0, which means that only the first byte is preserved and the other 3 bytes are set to 0s. The network address is 23.0.0.0.

## Slide 31
TCP/IP Protocol Suite
<number>
Given the address 132.6.17.85, find the beginning address (network address).
Example 13
Solution The default mask is 255.255.0.0, which means that the first 2 bytes are preserved and the other 2 bytes are set to 0s. The network address is 132.6.0.0.

## Slide 32
TCP/IP Protocol Suite
<number>
Given the address 201.180.56.5, find the beginning address (network address).
Example 14
Solution The default mask is 255.255.255.0, which means that the first 3 bytes are preserved and the last byte is set to 0. The network address is 201.180.56.0.

## Slide 33
TCP/IP Protocol Suite
<number>
Note that we must not apply the default mask of one class to an address belonging to another class.
Note: